## Slide 1
DT / STEM ROOM SAFETY
Year 7 Technology · Unit 3 — CyberPet for Wellbeing
What every student needs to know before hands-on work begins in Weeks 3–8.
St Peters Lutheran College Springfield

## Slide 2
Why this matters
Work Health and Safety
Act 2011 (Qld)
The law every Queensland classroom and workshop operates under — including this room, whenever tools, machinery or materials are in use.
Your teacher carries overall responsibility
for the safety of every activity in this room — that's why some steps (like laser cutting) are teacher-only, not student-run.
Supervision has to be active and “rescue-ready”
not just present in the room. That's why some tasks are staged separately rather than run all at once.
Equipment is used exactly as demonstrated
— never a shortcut you've seen elsewhere, and never before your teacher has shown you how.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
2

## Slide 3
Before you start: PPE & room rules
These apply every lesson, for every activity — not just the ones that feel risky.
Safety glasses when the task requires them
Worn any time a Safety Data Sheet or your teacher's instructions call for them — laser cutting, and some hand-tool work.
Enclosed footwear, always
No open sandals or thongs in the DT/STEM room — non-negotiable.
Hair tied back, no loose clothing or jewellery
Anything that could catch on a tool or machine comes off or gets tied back before you start.
Stay in your seated position while cutting
This room doesn't have marked exclusion zones, so staying seated keeps blades and moving parts away from other students.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
3

## Slide 4
Hand tools
SCISSORS & CRAFT KNIVES
LOW RISK
What to do
Cut cardboard and felt/synthetic leather only — never plywood or acrylic by hand
Craft knives: blades kept short, cutting done on a mat
Keep the blade moving away from your body at all times
Wait for your teacher's demonstration before cutting independently
Why this matters
Hard materials (plywood, acrylic) are never hand-cut — they're laser cut instead, specifically to keep sharp-blade work to soft materials only.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
4

## Slide 5
Laser cutter
TROTEC SPEEDY 300
TEACHER ONLY
What to do
You design in Tinkercad — your teacher does the actual cutting
Only approved plywood/acrylic is ever loaded
Lid interlock and fume extraction run for the whole cut
Cutting happens as a separate supervised batch, not while others use hand tools or glue
Students never operate this machine
This is the one manufacturing decision you explain and design for, rather than personally run — the room can't safely supervise the laser and hand-tool work at the same time.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
5

## Slide 6
3D printer
ADDITIVE MANUFACTURING
LOW RISK
What to do
Your teacher loads the file and operates the printer
Never touch the nozzle, the bed, or a print that's still in progress
Only handle a finished print once your teacher confirms it has cooled
Stay clear of the printer's position in the room while it's running
The nozzle and bed run hot
Typically 200–260°C — hot enough to burn on contact. Normal use never requires you to touch either part, so don't.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
6

## Slide 7
Adhesive
PVA / CRAFT GLUE
LOW RISK
What to do
Year 7 uses PVA or craft glue only — not hot glue guns
No heat involved, and the glue itself is non-toxic
Don't touch your eyes or eat while you have glue on your hands
Wash hands after use, as with any classroom material
Not the same as older year levels
Year 8/9 students use hot glue guns in this room under a different set of controls (gun stands, gloves, closer supervision) — that doesn't apply to this unit.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
7

## Slide 8
Electronics
MICRO:BIT + GLOWBIT + BATTERY
LOW RISK
What to do
Low-voltage battery power only — this design never uses mains power
GlowBit connects to the micro:bit's edge connector — no soldering involved
Wire your board using the teacher-provided starter script and demonstration
Never open or modify the battery pack itself
Lowest-risk activity in the unit
No mains power and no soldering means the main rule is simple: follow the wiring demonstration exactly as shown.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
8

## Slide 9
Know your risk levels
Every activity in this unit has already been risk-assessed by your teacher. Here's what the levels mean.
LOW
Minor, easily managed
Routine supervision handles it — this covers every activity in this unit as planned.
MODERATE
Needs some intervention
Contained quickly with a small, specific control — e.g. a teacher check-in before independent work.
HIGH
Significant, acts fast
Requires a qualified supervisor and tighter controls — this is why the laser cutter is teacher-only.
EXTREME
Serious consequences
Would mean stopping the activity entirely — not expected in this unit when controls are followed.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
9

## Slide 10
If something goes wrong
Report every injury, straight away
Even something minor — a small cut, a splinter, a bump. Tell your teacher immediately, every time.
Know where first aid is kept
Your teacher will point it out in your first lesson in this room — make sure you know before you need it.
Know your exits
Standard for every specialist room — if you're ever unsure, ask.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
10

## Slide 11
Where these rules come from
This isn't just classroom convention — it follows Queensland's actual safety framework for school workshops.
Work Health and Safety Act 2011 (Qld)
The legislation every Queensland workplace and school operates under, including specialist rooms like this one.
Practical Workshop Activities guideline (Queensland Dept of Education)
Sets out PPE requirements, supervision levels by risk, exclusion zones, and hazard categories for school workshop activities — the framework this room's own practices are aligned with.
QCAA Technologies P–10 syllabus
Requires safe, ethical practical work as a built-in part of the Design and Technologies learning area — not an optional extra.
This unit's own Risk Assessment
Year 7 Technology — CyberPets Unit 3 — the specific hazards and controls on the previous slides come directly from this document, completed by your teacher.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
11

## Slide 12
Before Week 3 starts, you should be able to...
Name the PPE and room rules that apply every lesson
Explain why the laser cutter and 3D printer are teacher-operated only
Describe the correct technique for hand-cutting with scissors or a craft knife
State what to do immediately if you or someone else is hurt
Explain, in your own words, why these rules exist
Questions? Ask your teacher before you start — not after.
St Peters Lutheran College Springfield · Year 7 Technology, Unit 3
12